## Slide 1: 1. Introduction
Fondamenti di Elettronica
Sergio Spanò – spano@ing.uniroma2.it

## Slide 2: Who I am
Sergio Spanò
  spano@ing.uniroma2.it
Ingegneria della Informazione
  Room B2-10 (2nd floor)
Reception on demand

## Slide 3: Info about the course
Fundamentals of Digital Electronics
  3 CFUs
  Written+oral exam
Book: Introduction to Digital Systems - Milos D. Ercegovac, Tomas Lang, Jaime H. Moreno
  Digital copies can be found online
  Some copies are available at our Library
  Hard copies sold by www.libreriaefesto.com
    The bookstore is located in San Paolo - Rome

## Slide 4: 1.1 Introduction

## Slide 5: Analog and Digital Electronics
The main task of the Electronic is the processing of signals.
Signal: is a mathematical function that expresses the variation of a quantity (temperature, pressure etc.) with respect to another (usually time).
Analog Electronic: it is based on continuous signals (analog signals) in terms of voltage and/or current.
Digital Electronic: it is based on discrete signals (both on the x and the y axis):
  digital signals are often derived by an analog ones;
  digitalization of analog signals is performed by three operations: sampling, quantization and coding.

## Slide 6: Analog to Digital conversion
Analog signal features:
  Signal is defined on the entire x axis
  Signal can have any value on the y axis
Both x (time) and y values ∈ ℝ

## Slide 7: Analog to Digital conversion: Sampling
Sampling: reduction of a continuous signal to a discrete signal.
A discrete signal is obtained considering the values of analog signal only at discrete time
Time between two values (samples) id called Sampling Period.
The inverse of Sample Period is called sample Frequency
Sampling MUST respect the Nyquist–Shannon sampling theorem
  Let the highest frequency component, in hertz, for a given analog signal is fmax. According to the Nyquist Theorem, the sampling rate must be at least 2fmax, or twice the highest analog frequency component.

## Slide 8: Analog to Digital conversion: Quantization
Discretization of the amplitude.
Y axis is divided in N levels, namely quantization levels
Each sampled value is approximated at the nearest quantization level
The error introduced by the approximation is called quantization error

## Slide 9: Analog to Digital conversion: Coding
Each quantization level is coded using numbers using a binary representation.
Each number is coded with 0s and 1s (bit).
More bits imply more quantization levels
More quantization levels imply more accuracy
  The more bits are used for quantization, the less is the NOISE

## Slide 10: Example: Audio CD
Audio PCM coding
  The signal is not compressed (it’s not like mp3)
2 channels (left and rigth) – stereo sound
44100 Hz sample frequency
16 bits  65536 quantization levels
How many bits per second?
  Considering left and right channels:
  Bitrate: (Mega bit per second)
How many bits per minute?
How many MegaBytes per song (3 min)?

## Slide 11: Introduction to digital systems
An electronic system is composed by
  Analog IN.
  Analog to Digital Converter (ADC).
  Digital System (Microprocessor, DSP,FPGA,ASIC).
  Digital To Analog Converter (DAC).
  Analog OUT.

## Slide 12: Why digital?
Noise immunity: continuous signal can be transmitted and reconstructed without errors .
Scalability: in a digital system, a more precise representation of a signal can be obtained by using more binary digits (bits) to represent it.
Reconfigurability: systems implemented on digital devices can be controlled by software
  new features can be added without modifying the hardware.
Storage: storage of digital data is easier than analog ones
Integration: digital circuits allow to build very complex circuits in terms of number of components (more than 1,000,000,000 of transistor for a single chip).

## Slide 13: Introduction to digital systems: Digital Systems classification
Combinational Systems
  The output is a function just of the present input
Sequential Systems
  The output is a function also of the past input(s)
  Systems with memory
  They usually need a synch signal (e.g. CLOCK)
Sequential Systems have Combinational Systems inside!

## Slide 14: Abstraction Level
A Digital Circuit is composed by different modules. Each module can be analyzed using a different abstraction level.
  The abstraction level defines how much detail about the design is specified:
    system;
    module;
    gates;
    transistors;
    silicon.

## Slide 15: Abstraction Level: System
At system level a circuit is described in terms of its behavior:
  an entity that performs a specific operation
  we don’t know how the entity is inside
E.g. Quadratic Equation Solver Circuit:

## Slide 16: Abstraction Level: Module
At module level a circuit is described as a connection of modules performing specific operations:

## Slide 17: Abstraction Level: Gates
At gate level a circuit is described in terms logic gates.
  Each module is composed by logic gates.
Adder

## Slide 18: Abstraction Level: Transistor
At transistor level a circuit is described in terms transistor.
  Each logic gate is composed by transistors.

## Slide 19: Abstraction Level: Silicon
At silicon layer a circuit is described in terms semiconductors.
  Transistors are composed by semiconductors.

## Slide 20: Silicon example
Intel i7 processor
  731.000.000 transistor in 263 mm²

## Slide 21: Abstraction Level: Top-down/Bottom up
Analysis can be performed using two different approaches
  Top-down: circuit is analyzed from system level to transistor level.
  Bottom-up: circuit is analyzed from transistor level to system level

## Slide 22: Recap
In this lesson we analyzed the basic concepts of digital systems.
An analog signal can be digitalized by the analog to digital conversion process.
Digital systems can be classified in:
  combinational systems;
  sequential systems.
Digital systems can be analyzed and designed at different abstraction levels.