## Slide 1: 2. Combinational systems
Fondamenti di Elettronica
Sergio Spanò – spano@ing.uniroma2.it

## Slide 2: Digital System: generic architecture 1/2
A digital system in composed by
  Input Coding
  Computation element
  Output decoding

## Slide 3: Digital System: generic architecture 2/2
Example: automatic radiator manager
  If the temperature is <= 10°C =>Radiator On else Radiator Off

## Slide 4: Digital System: combinational system 1/2
In combinational systems the output is function only of the present input
  Z(t)=f(X(t))
In other words, the outputs don’t depend on the history of the system.
  The system is without memory.

## Slide 5: Digital System: combinational system 2/2
Combinational system can be represented using different methods:
  Tables
  Arithmetic expressions
  Conditional expressions
  Logical expressions

## Slide 6: Boolean functions
Combinational system can be implemented using Boolean functions (Switching functions)
A Boolean function is a function which inputs and output can assume only the value 0 or 1

## Slide 7: Boolean functions: One input Boolean functions
Four 1 bit Boolean functions can be defined:
  Always 0
  Equal to x (Buffer)
  Not (Inverter)
  Always 1

## Slide 8: Boolean functions: Two inputs Boolean function
Sixteen 2 bit Boolean functions are defined. Among these, only 6 are frequently used:
  And
  Xor
  Or
  Nor
  Xnor
  Nand

## Slide 9: Boolean functions: Logic Gates
Boolean functions can be identified by a switching expression or by a symbol called Logic gate
  Logic gates are circuits composed by electronic components that perform the relative switching expression
Note:
Negation is also indicated as instead of x’

## Slide 10: Boolean functions: N inputs Boolean function
Logic gates can be generalized for N inputs
Usually for physical reasons N is limited (about 8)

## Slide 11: Boolean Algebra
Properties:

## Slide 12: Minterms
Literals: A single boolean variable
  x, x’, z, y’….
Product terms: product of boolean variables
  x, x0x1 , x0x1’ …
Sum of Products:
  x1+x0x1+x1x3
Minterm: A minterm of n variables is a product term of n literals containing each variable once in it, both negated or not
  Ex n=3  8 minterms m0,m1..m7
  x2x1x0 x2’x1x0 are minterms
  x2x1 x0x2 are not minterms

## Slide 13: Minterms: m-notation
Each minterm has a 1 value only for one assignment of the variables
  Ex m3 1 if x2’x1x0 =011

## Slide 14: Minterms: sum of minterms
A sum of minterms contains only not repeated minterms

## Slide 15: Maxterm
Sum terms: sum of boolean variables
  x, x0+x1 , x0+x1’ …
Products of Sum :
  (x1+x0+x1)(x1+x3)
Maxterm: A maxterm of n variables is a sum of n literals containing each variable once, both negated or not negated
  Ex n=3  8 maxterms M0,M1..M7
  (x2+x1+x0) (x2+x1+x0) are maxterms
  (x2+x1) (x0+x2) are not maxterms

## Slide 16: Maxterms: product of maxterms
Also Mamxterms have an M-notation, so M3 0 if x2’+x1+x0 =100 (complement of minterm)
A product of Maxterms contains only not repeated Maxterms

## Slide 17: Terms and Switching functions
Functions can be represented using Minterms or Maxterms
  If a function is incomplete, it is possible to use the don’t care (-)
or

## Slide 18: Design example 1/5
G=GREATER
E=EQUAL
S=SMALLER
FUNCTION
Design a digital comparator

## Slide 19: Design example 2/5

## Slide 20: Design example 3/5

## Slide 21: Design example 4/5
Z2 =X1’X0Y1’Y0’+X1X0’Y1’Y0’+X1X0Y1’Y0’+ X1X0’Y1’Y0 + X1X0Y1’Y0+X1X0Y1Y0’
Z1=…….
Z0=…….

## Slide 22: Design example 5/5
Z2 =X1’X0Y1’Y0’+X1X0’Y1’Y0’+X1X0Y1’Y0’+ X1X0’Y1’Y0 + X1X0Y1’Y0+X1X0Y1Y0’
Z2=